Date: 18 January 2024
Author: Christiaan van der Tol
Description: This folder contains the Matlab code of the Band Shape Fitting method (BSF) for the retrieval of fluorescence from hyperspectral upwelling and donwelling radiance from tall towers.

Reference:
van der Tol, C., Julitta, T., Yang, P., Sabater, N., Reiter, I., Tudoroiu, M., ... & Drusch, M. (2023). Retrieval of chlorophyll fluorescence from a large distance using oxygen absorption bands. Remote Sensing of Environment, 284, 113304.

1. Introduction

Band Shape Fitting is a method to differentiate infilling by fluorescence and deepening by oxygen absorption in O2 bands. The method is designed for the retrieval of F from towers, where atmospheric correction is needed.
The algorithm is describe in detail in a paper by C. van der Tol et al.. This document is a user manual for the code.
The code is written in Matlab2017a.

2. The main code

The main function of the altorithm is retrievalF.m

This function is called by scripts starting with ‘master..’, which prepare the input for a specific experiment. They load FLOX box L1b data, prepare the input for BSF, estimates prior values for the atmospheric optical path length, and save the output data. Some also contain a section in which SCOPE can be run (which in turn uses ephoton and e2phot). The function master_selecteddays carried out all time series simulation that are presented in the paper.
The following master scripts have been used in the study:

master_selectedays_revision.m: this script was used in the paper (See reference) to run BSF on the data of the so called OHP capaign in France.
master_synthetic: reads the synthetic dataset of DEFLOX, and runs BSF on the data
master_synhtetic_Cabauw: reads the synthetic diurnal cycles mimicking Cabauw, and runs BSF on these
master_cabauw2: runs BSF on the entire folder of Cabauw FLoX measured data and stores the output.

The master scripts can be used as an example to run retrievalF.

retrievalF uses:
Set_parameters.m: to specify the shoulder locations of the bands
Cost4F: the cost function
iFLD: for comparison, the function also applies the iFLD method

The required input for the function retrievalF.m includes:
This function requires as input:
- The wavelength of the measurement, which must include the range from the left to the right shoulder of both bands (O2A or O2B). This must be a vertically oriented array.
- The corresponding spectrum of measured irradiance E (in the same unit as piL). This must be a vertically oriented array.
- The corresponding spectrum of measured upwelling radiance piL (in the same unit as E). This must be a vertically oriented array.
- Options for the iteration (such as the stopping criterion) for the function ‘lsqnonlin’, notably: opt = optimset('MaxIter',30,'TolFun',1E-4);
- The prior value of the relative atmospheric path length a
- The cosine of the solar zenith angle
- The cosine of the viewing angle of L
- The weight of the prior value of a (between 0 and inf, use ‘0’ as default value)
- A structure of parameters that includes at the left and right shoulder wavelengths of the band of both bands (see function ‘parameters’ below).
- SRCA and SRCB: sensor specific correction functions for the spectral response function, calculated with SRF_correction3.m

The output of the function is two structures, O2A and O2B, containing:
- wl: the wavelengths of the measurement within the band ranges
- F: the retrieved fluorescence
- E: the measured downwelling irradiance
- piL: the measured upwelling radiance times pi
- piLr: the measured upwelling radiance times pi, less the fluorescence
- normpiL: the upwelling radiance normalized by the shoulders
- normE: the downwelling irradiance normalized by the shoulders
- a: the retrieved atmospheric optical path length
- EXITFLAG: the output flag of the Matlab buitin function ‘lsqnonlin’
- iFLD: the fluorescence of the iFLD method (for comparison to the BSF method)

The function is called as follows:
[O2A, O2B] = retrievalF(wl,E,piL,opt,aprior,cos_sza,cos_vza,priorweight,p ,SRCA,SRCB,flwf);
The supporting function set_parameters.m specifies the left and right shoulders of the O2A and O2B band. The other lines in this function are not needed for BSF, but they are parameters for the iFLD method, and they are included for completeness. In the script of the paper, these are used to calculate iFLD fluorescence for the same measurements.
parameters.wl_left = [759, 686.5]; % just left, used in BSF
parameters.wl_right = [768, 688.1]; % just right, used in BSF
parameters.wl_in = [761,686.9]; % next 6 coefficients are all used in iFLD
parameters.wl_out = [755,686.5];
parameters.wl_left0 = [750,680];
parameters.wl_left1 = [755,686.5];
parameters.wl_right0 = [772,688.1];
parameters.wl_right1 = [777,690];

The function cost4F which is called by retrieval contains the cost function to be minimized. This code subtracts fluorescence (as input) from the measured radiance, then carried out linear regress of log radiance versus log irradiance, uses the slope of the linear regression to model the upwelling radiance, and finally calculates the difference between modelled and measured upwelling radiance. This difference is a vector with the dimensions of the wavelengths of the measurements in the band. The difference between the prior value of the atmospheric path length ‘a’ and the slope of the linear regression is added with a weight ‘w’ (see the paper for details).

The use is as follows:
[e,a,ymod] = cost4F(F,input)
Where the input is:
F is the fluorescence in the same unit as the irradiance, and input a structure containing the following (all are calculated within retrievalF.m):
Logx : the logarithm of the normalized irradiance
Y: the upwelling radiance
cos_sza: the cosine of the solar zenith angle
cos_vza: the cosine of the viewing zenith angle
fwlf: a function that describes the shape of the fluorescence spectrum over the O2 band
normpiL: the spectral shape of the upwelling radiance interpolated between the shoulders of the O2 band
The output includes the cost function ‘e’ (‘e’ stands for error here), the slope of the regression ‘a’, and the modelled upwelling radiance without fluorescence ymod.
Other supporting functions are provided to apply the model. These are not essential, but they are useful to prepare inputs for the model.

3. Other supporting functions

The function SRF_correction3.m produces a file for the error correction caused by the convolution and the spectral response of the instrument. This is slightly dependent on the instrument, and the files can be generated with information on the location of the bands and the spectral resolution of the instrument. The file produces SRCA and SRCB for the O2A and O2B bands, respectively. The files SRCA and SRCB each contain a spectrum, and coefficients that parameterize the relation of the correction with the solar zenith angle (field ‘c’ in SRCA.mat and SRCB.mat).
SRF_correction3.m uses MODTRAN files that are also provided with the code (.tp5 and .atm files).

The function plot_F_final reproduces nearly all figures of the paper.
The function plot_barometric reproduces figure 3 of the paper.
The supporting functions used in master_selecteddays are:
readFXBox: a function that scans a FLOXboxfile, and returns the data as matlab variables. Usage: [wl, data, time] = readFXBox(filename)
calczenithangle: a function that calculates the solar zenith angle from the geographical location and the date and time.
set_parameters: a function that specifies the wavelengths of the shoulders of the O2 bands.
Barometric: contains the barometric equation, which in turn uses set_constants.
The function run_and_plot_sensitivity carries out a sensitivity analysis of BSF and plots a figure for the paper.